## Slide 1
Lab 3B
From vibration signals
to spectral features
Frequency-domain feature engineering for beginner Strategic Engineering MSc students
Scenario: 100 Hz vibration monitoring of a rotating machine — compare normal and fault-like windows.
Notes: [Sources] - User-provided Lecture 3, slides 69–95 [/Sources] Title slide for the lab package.

## Slide 2
Engineering scenario
The same waveform can look similar in time while differing strongly in frequency content.
Normal condition
Dominant rotational component around 10 Hz
Weak harmonics
Low high-frequency energy
Fault-like condition
Same main rotation
Stronger 2nd/3rd harmonics
More high-frequency energy
Decision question
Which compact, interpretable features would preserve the useful condition information?
time window
spectrum
features
later model
This lab stops at feature construction and interpretation.
Notes: [Sources] - User-provided Lecture 3, slides 69–95 [/Sources] Synthetic teaching scenario; no claim of diagnostic validity for a specific physical fault.

## Slide 3
Learning objectives
1
Sampling
Connect Fs, Δt and the Nyquist limit.
2
Spectrum
Compute a one-sided FFT and interpret its peaks.
3
Resolution
Relate window duration to frequency-bin spacing.
4
Features
Extract dominant frequency and band-power features.
5
Leakage
Observe spectral leakage and the effect of a Hann window.
6
Representation
Combine time- and frequency-domain features and discuss information loss.
Notes: [Sources] - User-provided Lecture 3, slides 69–95 [/Sources] Objectives mirror the concepts covered across Lecture 3 slides 69–95.

## Slide 4
Core workflow
A frequency-domain feature pipeline is an explicit engineering design.
Temporal
window
Remove mean
/ detrend
FFT
Magnitude /
power spectrum
Spectral
features
Examples of final features
dominant frequency
total spectral energy
band power
relative band power
The feature designer chooses the window, preprocessing and frequency bands.
Notes: [Sources] - User-provided Lecture 3, slides 69–95 [/Sources] Workflow corresponds to the lecture section on FFT-based feature engineering.

## Slide 5
Sampling essentials
The frequency axis has physical meaning only when the sampling rate is known.
Fs
100 Hz
100 frames each second
Δt = 1/Fs
0.01 s
between consecutive frames
Nyquist
Fs/2 = 50 Hz
highest unique frequency
Resolution
Δf ≈ Fs/L
set by window length
0
10
20
30
40
50
frequency [Hz]
Nyquist
Above 50 Hz, components do not disappear harmlessly — they can alias into lower frequencies.
Notes: [Sources] - User-provided Lecture 3, slides 69–95 [/Sources] Uses the sampling-rate and Nyquist concepts from the lecture.

## Slide 6
Window duration controls frequency resolution
Longer windows separate nearby frequencies more finely, but localize changes less precisely in time.
1 s window → Δf = 1 Hz
Chart: 
| 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
spectrum | 0.02 | 0.04 | 0.2 | 1 | 0.82 | 0.18 | 0.04 | 0.02
10.0 and 10.8 Hz are difficult to distinguish.
4 s window → Δf = 0.25 Hz
Chart: 
| 8.5 | 9 | 9.5 | 10 | 10.25 | 10.5 | 10.75 | 11 | 11.25 | 11.5 | 12
spectrum | 0.02 | 0.05 | 0.18 | 1 | 0.3 | 0.08 | 0.22 | 0.78 | 0.2 | 0.05 | 0.02
The nearby components become more separable.
Trade-off: frequency resolution ↑ ↔ temporal localization ↓
Notes: [Sources] - User-provided Lecture 3, slides 69–95 [/Sources] Illustrative spectra; values are schematic rather than measured data.

## Slide 7
What features will we extract?
Interpret the spectrum as engineering information, not just as a plot.
Dominant frequency
Where is the strongest spectral component?
Band power
How much energy lies inside a chosen frequency interval?
Relative band power
Band power / total power — less dependent on overall amplitude.
Teaching bands for the synthetic 100 Hz signal
0–15 Hz
low band
15–30 Hz
mid band
30–50 Hz
high band
Fault-like synthetic windows are designed to show stronger harmonics and higher-band energy.
Band definitions should come from physical knowledge or later validation — not from the test set.
Notes: [Sources] - User-provided Lecture 3, slides 69–95 [/Sources] Feature definitions follow the lecture examples. Band limits are chosen for the synthetic lab data.

## Slide 8
Spectral leakage and the Hann window
Finite windows can spread energy across nearby frequency bins.
Chart: 
| 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
No window | 0.02 | 0.03 | 0.05 | 0.08 | 0.15 | 0.42 | 1 | 0.9 | 0.35 | 0.14 | 0.08 | 0.05 | 0.03
Hann | 0 | 0 | 0.01 | 0.01 | 0.04 | 0.22 | 0.85 | 1 | 0.56 | 0.1 | 0.02 | 0 | 0
Without window
Boundary discontinuity can create stronger sidelobes: energy appears farther from the true component.
With Hann
Distant leakage is reduced, but the main peak becomes broader.
Cleaner spectrum away from the peak ↔ slightly poorer separation of very close frequencies
Notes: [Sources] - User-provided Lecture 3, slides 69–95 [/Sources] Schematic illustration of leakage and windowing trade-off from the lecture.

## Slide 9
Lab roadmap
Work in pairs; focus on interpreting every plot and feature.
1
Sampling
Compute Δt and Nyquist.
2
FFT
Build the physical frequency axis.
3
Resolution
Compare 1 s and 4 s windows.
4
Features
Extract dominant frequency and band powers.
5
Leakage
Compare raw and Hann-windowed spectra.
6
Feature table
Combine RMS/statistics with spectral features.
7
Interpret
Explain what is gained and what is lost.
No classifier is required in this lab.
Notes: [Sources] - User-provided Lecture 3, slides 69–95 [/Sources] Final intro slide; later lecture material covers conventional supervised models.